## Slide 1: SISTEMAS OPERATIVOS
SO
E – M 2019

## Slide 2: OS Processing Concepts - 1
Monoprogramming and Multiprogramming
  amount of processes in memory
Synchronous I/O, Asynchronous I/O and Asynchronous I/O Time Sharing
  CPU execution method for a process with I/Os
Monouser and Multiuser
  total of users being served

## Slide 3: OS Processing Concepts - 2
Multiprogramming
Time Sharing
Functional Characteristics

## Slide 4: Memory Layout for Multiprogrammed System

## Slide 5: Operating System Structure
Multiprogramming needed for efficiency
  Single user cannot keep CPU and I/O devices busy at all times
  Multiprogramming organizes processes (code and data) so CPU always has one to execute
  A subset of total processes in system is kept in memory
  One process selected and run via process scheduling
Timesharing is logical extension in which CPU switches jobs so frequently that users can interact with each job while it is running, creating interactive computing
  Response time should be < 1 second
  Each user has at least one program executing in memory process
  If several processes ready to run at the same time  CPU scheduling
  If processes don’t fit in memory, swapping moves them in and out to run
  Virtual memory allows execution of processes not completely in memory
  When it has to wait (for I/O for example), OS switches to another job

## Slide 6: OS Operations 1
Interrupt driven (hardware and software)
  Hardware interrupt by one of the devices
    Power on
    I/O devices, finished task
    DMA, finished task
    Hardware fails
    Exhausted Processing clock
    Others …
  Hardware Interrupt: notification of a finished event
  The CPU switches, from what it is doing, to a Kernel Routine
  Uses the Interrupt Vector to pick up the values for the PC and PSW to switch into a Kernel Routine.

## Slide 7: OS Operations 2
Interrupt driven (hardware and software)
  Software interrupt (exception or trap):
    Request for operating system service
      Starting an I/O
      Shutdown
      To invoke any Kernel routine ( open, run, mkdir, fork, …)
    Software error
      Arithmetic overflow, underflow
      Zero division
      Illegal instruction
      Memory address violation
  The software interrupt is provoked inside a process / program
  Software Interrupt: to initiate or finish an event
  The CPU jumps into a Kernel Routine (System Call function)
  Uses the Interrupt Vector to pick up the values for the PC and PSW to switch into a Kernel Routine.

## Slide 8: OS Operations (cont.)
Dual-mode operation (hardware) allows OS to protect itself and other system components
  User mode and kernel (privileged) mode
  Mode bit provided by hardware (PSW register)
    Provides ability to distinguish when system is running user code or kernel code
    Some instructions designated as privileged, only executable in kernel mode
    System call changes mode to kernel, return from call, resets it to user

## Slide 9: Dual mode operation
Mode bit in PSW register: kernel (0), user(1)
Trap: program switches to kernel mode
Interrupt: hardware switches to kernel mode
kernel
user
Trap
set user mode
Interrupt
Controller

## Slide 10: Trap from User to Kernel Mode

## Slide 11: References
Presentación de Ramon Ríos.
Capítulos: Operating System Concepts; Silberschatz, Galvin, Gagne.
24 enero 2019