## Slide 1: SISTEMAS OPERATIVOS
SO
E – M 2019

## Slide 2: Computer System Architecture
Normal architecture – CPU (Control Unit), ALU, registers, storage unit, I/O devices, etc.….
Von Neumann’s – contribution
  The addition of a stored-program in a single separate memory structure that keeps both instructions and data.
  The computers that follow the "von Neumann architecture" are also known as the “Stored-Program Computer“.
Registers

## Slide 3: Von Neumann’s architecture + Bus
Components of a General Purpose Computer System
  Except CPU, every component has a Controller
  Each Controller has: registers and a buffer, to take care of the Inputs and Outputs of the devices.
Bus
Monitor
controller
Stored-program

## Slide 4: Computer Structure
*PC
CPU
Buffers
I/O Module Controllers
Memory
Instruction
Instruction
Instruction
Data
Data
Data
Data
.
.
.
.
.
IR
MAR
MBR
I/O AR
I/O BR
execution
unit
.
.
.
.
.
.
MAR - Memory Address Register
MBR - Memory Buffer Register
I/O AR - I/O Address Register
I/O BE - I/O Buffer Register
PC - Program Counter
IR - Instruction Register
SP – Stack Pointer
*Must be saved and restored
0
N
1
*SP
*PSW
BUS
Stored-program

## Slide 5: How a Computer Works
A von Neumann architecture

## Slide 6: Multiprocessor Architecture
Several processors processing, one shared memory. One Computer System.
General purpose computer system
Every processor services a process for a time slice, next time could serve a different process.
Is there any issue with the shared memory? _____
One-Core/chip.

## Slide 7: A Dual-Core Design
One-chip / multicore
Traditional: One-thread / core
  Increase of processing : Two-threads / core
  After math: Two-cores / chip & Two-threads / core = ___

## Slide 8: Parallel Systems
Multiprocessors systems growing in use and importance
  Also known as parallel systems, tightly-coupled systems
  Advantages include:
    Increased throughput
    Economy of scale
    Cooperative parallel applications - (e.g. vectorization).
  Two types:
    Asymmetric Multiprocessing – each processor is assigned a specific task.
    Symmetric Multiprocessing – each processor performs all tasks

## Slide 9: Clustered Systems
External Buses
External Buses

## Slide 10: Clustered Systems
Multiple Computer Systems working together
  Need an external bus to link the clustered computers
  Usually sharing storage via a storage-area network (SAN, NAS)
  Provides a high-availability service which survives failures
    Asymmetric clustering has one machine in hot-standby mode
    Symmetric clustering has multiple nodes running applications, monitoring each other

## Slide 11: References
Presentación de Ramon Ríos.
Capítulos: Operating System Concepts; Silberschatz, Galvin, Gagne.
29-ene-2019